## Slide 1: Energy Efficiency: Linkages with DSM, Methods, Technologies, Role of CSOs in West Bengal
Dilip Samajpati
CESC Limited
March 13, 2012

## Slide 2: Demand Side Management
During 24 hours in a day, the demand for power changes over various time periods. It usually reaches the peak in the evenings when the lighting load is added to other loads. Demand Side Management (DSM) is a process to manage this variation in demand by planning and monitoring the pattern of electricity usage by the consumers.
The simplest way of managing peak demand in the evenings is to control the use of high consumption electrical equipment (e.g. Air Conditioner, Geyser and other heating appliances, Pumps etc wherever possible.

## Slide 3
DSM is the modification of consumer demand for energy through various methods such as financial incentives and education.
General perception, it is an activity beyond meters where a distribution company has very little or no control.

## Slide 4
TOD Tariff
Power Factor Rebate / Surcharge
Load Factor Rebate / Surcharge
Less tariff for energy efficient equipment
(Street Lighting with LED – 46 P less)

## Slide 5
Direction to create awareness on TOD tariff
Direction for installation of capacitor banks by the consumers
Direction for installation of capacitor banks by the licensee
Direction for energy audit
Direction for undertaking load research

## Slide 6
Encouraging TOD
Encouraging Energy Audit at Consumers’ establishments
Informing about installation of Capacitors for improvement of power factors
Metering of Street lighting supplies
Intense drive against theft of electricity

## Slide 7: TOD Tariff
CESC is actively encouraging TOD tariff in line with the directives of the Hon’ble WBERC.
TOD tariff scheme is a tool for DSM as the scheme adopts higher prices during peak hours to discourage consumption.
Concessional rates adopted during off-peak hours encourage consumption and smoothens the demand curve.
Consumer may re-engineer their drawal from peak hours to off-peak hours to avail of the benefit of overall reduction in their electricity bill.

## Slide 8: TOD for Industrial Consumers
As per Tariff Order of 2010 – 2011
Period | Time Zone | Energy Charge (Paise/kWh)
Normal | 0600 hrs. to 1700 hrs. | 521
Peak | 1700 hrs to 2300 hrs. | 782
Off-peak | 2300 hrs. to 0600 hrs. | 359

## Slide 9: TOD for Commercial Consumers
As per Tariff Order of 2010 – 2011
Period | Time Zone | Energy Charge (Paise / kWh)
Normal | 0600 hrs. to 1700 hrs. | 540
Peak | 1700 hrs to 2300 hrs. | 594
Off-peak | 2300 hrs. to 0600 hrs. | 502

## Slide 10
Load research is the study of how consumers and groups of consumers use electricity
Involves measurement and study of the characteristics of electric loads of the consumers.
Helps understanding and predicting how customer loads behave
Required for DSM interventions

## Slide 11
Lighting Load 300-350 MW
  Street Light : 50 MW
  Domestic & Commercial Load : 300 MW
Municipalities : 100 MW
  Pumping Stations
  Drainage P.S.
  Utilities
AC and Fan load – Domestic : 450-500 MW
Power factor improvement

## Slide 12: Bureau of Energy Efficiency
The mission of Bureau of Energy Efficiency (BEE) is to institutionalize energy efficiency services, enable delivery mechanisms in the country and provide leadership to the key players involved in the energy conservation movement. The primary goal of the Bureau is to reduce the energy intensity in the economy of the country.

## Slide 13: Electrical Rating for Refrigerator (250 Litres Frost Free)
Star Rating | Approx. Maximum Annual Energy Consumption | Per Unit Charge in Rs. (approx.) | Total Cost per year in Rs. | Total Saving (w.r.t No Star) Every Year in Rs.
No Star | 1100 | 4.00 | 4400 | 0
1 (One) | 977 | 4.00 | 3908 | 492
2 (Two) | 782 | 4.00 | 3128 | 1272
3 (Three) | 626 | 4.00 | 2504 | 1896
4 (Four) | 501 | 4.00 | 2004 | 2396
5 (Five) | 400 | 4.00 | 1600 | 2800

## Slide 14: Electrical Rating for Tube Lights
BEE STAR RATING PLAN |  |  |  |  | 
STAR RATING | * | ** | *** | **** | *****
Lumens per Watt at 100 hrs of use | <61 | >=61 & <67 | >=67 & <86 | >=86 & <92 | >=92
Lumens per Watt at 2000 hrs of use | <52 | >=52 & <57 | >=57 & <77 | >=77 & <83 | >=83
Lumens per Watt at 3500 hrs of use | <49 | >=49 & <54 | >=54 & <73 | >=73 & 78 | >=78

## Slide 15: Electrical Rating for Air - Conditioner
Star Rating | Max. | Min. | Input Power | Unit Consumed/Day in KWh (app.) | Charge/ Unit in Rs. (app.) | Total Expenditure in Rs. | Total Saving (without W.R.T. star) per year in Rs.
 | Cooling Capacity (in Watt) | Electricity Efficiency Ration (EER) |  |  |  |  | 
Without Star | 5200 | 2.20 | 2364 | 18.91 | 4.00 | 2269 | 0
* | 5200 | 2.30 | 2261 | 18.09 | 4.00 | 2170 | 987
** | 5200 | 2.50 | 2080 | 16.64 | 4.00 | 1997 | 2723
*** | 5200 | 2.70 | 1926 | 15.41 | 4.00 | 1849 | 4202
**** | 5200 | 2.90 | 1793 | 14.34 | 4.00 | 1721 | 5477
***** | 5200 | 3.10 | 1677 | 13.42 | 4.00 | 1610 | 6588

## Slide 16: Using Energy Efficiently
Switching off electrical appliances when not required will reduce consumption.
Use tube lights or energy saving lamps, such as CFL (Compact Fluorescent Lamp). This is applicable for A.C. supplies only.
Use of electronic chokes with tube lights and electronic regulators with ceiling fans reduces consumption of electricity.
Frequent opening of refrigerator door should be avoided.
Keeping TV, Computer etc. on stand-by mode should be avoided because it consumes power in that mode also.

## Slide 17: Using Energy Efficiently - contd.
Clean the lamps, bulbs and its reflectors regularly.
Use more sunlight. By doing so, you can avoid using electricity to illuminate your home or office during the day.
Use white or light colours for the walls, ceilings, curtains, drapes and furniture as they help retain more light within the building and therefore, further reduce the cost of lighting.
Use domestic appliances which conform to ISI standards.

## Slide 18: Using Energy Efficiently - contd.
Iron your clothes and linen at one go. Do not keep the hot iron upright for long.
Before putting anything in the refrigerator, allow it to cool to room temperature and stack food items inside the refrigerator in such a way so as to allow adequate air circulation.
Clean the air filter of the air-conditioner regularly. It increases compressor efficiency.

## Slide 19
Thank You