## Slide 1
ENERGY EFFICIENCY
ACTIVITY TIME

## Slide 2
Before we start with the activity some basic terms are explained here:
Wattage (w): Mentioned in the equipment for e.g. A 40 Watt bulb, an 18watt CFL etc.
Kilowatt (Kw): When the wattage is divided by 1000, you get Kw. e.g.
The Kw of a 40 w bulb is 40/1000 Kw and for an 18 w CFL is 18/1000 Kw.
Kilowatt Hour (KwH): When the Kw is multiplied by the hours of usage of the equipment what we achieve is known as KwH.
For e.g. if we use the 18 W CFL bulb for 8 hours a day, the KwH for an 18 W CFL will be (18/1000 x 8 hours).
KwH for a Month will be (18/1000 x 240 hours{8 hrs. x 30 days a month})

## Slide 3
Calculation of Electricity consumption per Month
Watt/1000 X Running Hours per Month = Units Consumed/ Month
* Days per Month : 30
* Running Hours : Depends on the usage of the equipment

## Slide 4: A CASE STUDY
Ram and Rahim are neighbours.
They both have identical houses and electrical usages.
Even after having so much similarity, it was found that Ram’s electricity bill was way higher than that of Rahim’s.
This led Ram to introspect what Rahim did to save his electricity consumption.

## Slide 5
Sl. No. | No. of Equipments | Electrical Equipments | Running time (Hours/ Day) | Wattage of the equipment | 
 |  |  |  | Ram | Rahim
1 | 3 | Incandescent bulb | 8 Hours | 40Watts | 
2 | 3 | CFL bulb | 8 Hours | - | 11 Watts
3 | 2 | Normal Fans | 6 Hours | 80Watts | -
4 | 2 | 5 Star labeled Fan | 6 Hours | - | 50 Watts
5 | 1 | Television (TV) | 4 Hours | 100 Watts | -
6 | 1 | 5 Star labeled TV | 4 Hours | - | 50 Watts
7 | 1 | Frost Free Fridge | 24 Hours | 125 Watts | -
8 | 1 | 5 Star labeled Frost Free Fridge | 24 Hours | - | 46 Watts
9 | 1 | 1.5 Ton AC | 2 Hours | 2368 Watts | -
10 | 1 | 1.5 Ton AC | 2 Hours | - | 1677 Watts

## Slide 6: Now let us study the usage of electricity of Ram
Sl.No. | Equipments (E) | Hours/ day (H) | Watt (W) | Units Consumed per month (W/1000 * Hours per Month) | Units/Month
1 | 3 Incandescent bulb | 8 | 40 |  | 
2 | 2 Fan | 8 | 80 |  | 
3 | Television | 4 | 100 |  | 
4 | Frost Free Fridge | 24 | 125 |  | 
5 | 1.5 Ton AC | 2 | 2368 |  | 
 |  |  |  | TOTAL CONSUMPTION PER MONTH | 

## Slide 7: Now let us study the usage of electricity of Rahim
Sl.No. | Equipments (E) | Hours/ day (H) | Watt (W) | Units Consumed per month (W/1000 * Hours per Month) | Units/Month
1 | 3 Incandescent bulb | 8 | 11 |  | 
2 | 2 Fan | 8 | 50 |  | 
3 | Television | 4 | 50 |  | 
4 | Frost Free Fridge | 24 | 46 |  | 
5 | 1.5 Ton AC | 2 | 1677 |  | 
 |  |  |  | TOTAL CONSUMPTION PER MONTH | 

## Slide 8: What is your conclusion?
A) Units saved per month by Rahim = ________
B) Units saved per year (A x 12) = __________
Total saving of Rahim per annum =
units saved x unit charge = Rs ______________
Assume Unit Charge = Rs 5.40. Let us round it to Rs 5.00

## Slide 9: Rahim’s Investment
Sl.No. | Equipments (E) | Price per piece (p) | Number of piece (T) | Total price of each item (T.P) T.P. = PxT
1 | CFL bulb | Rs. 130/- | 3 | 
2 | 5 star labeled Fan | Rs. 1450/- | 2 | 
3 | 5 star labeled Television | Rs. 13000/- | 1 | 
4 | 5 start labeled Fridge | Rs. 12000/- | 1 | 
5 | 1.5 Ton AC | Rs. 20000/- | 1 | 
 |  |  | TOTAL INVESTMENT | 

## Slide 10: Ram’s Investments
Sl.No. | Equipments (E) | Price per piece (p) | Number of piece (T) | Total price of each item (T.P) T.P. = PxT
1 | Incandescent bulb | Rs. 20/- | 3 | 
2 | Fan | Rs. 750/- | 2 | 
3 | Television | Rs. 5500/- | 1 | 
4 | Fridge | Rs. 7500/- | 1 | 
5 | 1.5 Ton AC | Rs. 15000/- | 1 | 
 |  |  | TOTAL INVESTMENT | 

## Slide 11: Let us now calculate Rahim’s Payback period
Rahim invested = Rs ___________ more
His savings per annum= Rs ______________
Recovery period in years = ___________years
(Invested amount / Savings)

## Slide 12: Conclusion
Rahim recovers his extra investment in _____
years, and continues to save Rs ____ every
year, but Ram has to go on paying Rs _____
more every year because he has not used Star
Labeled equipments.

## Slide 13
THANK YOU